## Slide 1: A Sustainable Planet
Week 9
Low Carbon Energy
Dr Vicky Coker
Department of Earth and Environmental Sciences
vicky.coker@manchester.ac.uk; Williamson Building

## Slide 3: Learning outcomes
Uranium
  Geology
  Mining
  Processing
Enrichment
Nuclear Fission
Pressurised water reactors
Comparison with fossil fuels
What to do with the waste?

## Slide 4
https://www.world-nuclear.org/information-library/current-and-future-generation/nuclear-power-in-the-world-today.aspx

## Slide 5
Nature and Origin of Nuclear Power What do nuclear reactors “burn”?
235U
=92 protons and 143 neutrons

## Slide 6: Uranium Occurrence
Crustal abundance of 2.7 ppm
Uranium is a large atom and only fits into certain minerals
e.g. apatite, zircons
Ore of uranium
  uraninite (UO2)
  pitchblende (U3O8)
  +many others
Variety of deposit types
uraninite

## Slide 7: Uranium: secondary formation
Most U formed in association with igneous rocks during late stage melt crystallization
However:
  Uranyl transported by groundwaters after leaching the uranium from the solid
  reduced downstream when conditions change = Precipitation of uranium back into a solid = hydrogenic
OR can be deposited as a placer deposit (similar to gold), where density separation concentrates uranium grains
U4+
U6+ /uranyl ion (UO2)2+
oxidation
SOLID
SOLUBLE
reduction

## Slide 8: Unconformity deposit: Athabascan Basin, Canada
Highest grade uranium deposits e.g. Cigar Lake = 16% U3O8
Form in association with the meeting point between metamorphic basement and a sedimentary basin = unconformity
longharbourexploration.com

## Slide 9: Roll front deposits: e.g. Australia, Kazakhstan
Roll-front deposits shape results from movement through a porous rock, e.g. sandstone, with dissolution and deposition along a curved front.
Mining: In situ leaching (ISL)
Inject a solution that oxidises, solubilises and binds the uranium, then it is pumped out e.g sulphuric acid leaching

## Slide 10: Purification and concentration of U ore
Dynamic treatment (High grade ore > 0.10%)
Crushed and ground mechanically
Processed with chemical solutions
Acid heap leaching (low grade ore-the rest)
.
Yellowcake
~0.7 % 235U
Solid, concentrated uranium is obtained called "yellow cake" containing around 75% uranium, or 750 kilograms per metric ton

## Slide 11: 235U Natural uranium 0.7 % 235U ; >99% 238U Pressurised Water Reactor - 3% 235U
?

## Slide 12: Uranium Enrichment / Fuel
Enrichment
  UF6 formation = energy intensive
  Gas diffusion to increase 235U concentration as isotopes have different weights
After gas diffusion, form (in PWR) fuel pellet (uranium dioxide ceramic), fuel rod and fuel assembly
2 – 4 % 235UO2
http://www.klimaatkeuze.nl/wise/monitor/439-440/paitz
UF6
1350C
-U235
+U235
Waste U238rich = depleted uranium

## Slide 13
Nuclear reactor 1 x 10n – controlled fission
235U + 10n  2 x F.P. + ~ 3 10n + energy
X
2 neutrons lost by escape / absorbed by control rods
Slow neutron induces nuclear fission (8x speed of sound)
X
1 neutron moderated and fissions with another 235U atom in the fuel

## Slide 14: Generic Pressurized Water Reactor (PWR)

## Slide 15
PWR Operation
Fission products “grown into” fuel, have high fission reaction cross sections, fission becomes inefficient
2 – 3 years spent nuclear fuel; radioactive waste
Spent fuel = ~3% FPs; ~1% Pu; 96% 235+238U
Spent fuel radioactive for 10,000y+  radioactive waste or reprocessing (“recycle”) to manage the waste component

## Slide 16
How does it compare to fossil fuel?
Chemical reaction ~4 eV per molecule e.g. combustion of fossil fuels
Nuclear reaction ~ 200,000,000 eV per molecule
1 g 235U is equivalent to ~2.5 t carbon
Nuclear = Carbon-free at the point of generation

## Slide 17: Nuclear waste
What are alpha, beta and gamma radiation?
Where does the waste come from?
How do we classify it?
Legacy waste issues in the UK
How is the UK going to dispose of the legacy nuclear waste?

## Slide 19
Radioactivity
The ‘half life’ is the time it takes for any given radioisotope to decay to half of its original activity
This varies between isotopes e.g. 99mTc = minutes, 237Np = millions of years

## Slide 20
Radioactivity was discovered in 1896 (Henri Becquerel)
There are 3 types of emission from radioactive decay-
alpha
beta
gamma
Particle radiation from nuclear reactions
- neutrons (important)
- fission products (less so)
Nuclear fission reaction discovered by Hahn and Strassmann in 1938
A “fissile” isotope is one which will undergo a fission reaction itself
A “fertile” isotope is one which can be converted by neutron capture into a fissile one
Radioactivity

## Slide 21
Alpha Decay
Alpha decay is characteristic of heavy nuclei (A > 200)-
●Decay energies are typically 3.5-6 MeV
●Alpha particles are heavy and highly charged so interact readily with matter and have only a short range (5 cm in air)
U Th + He
236
92
232
90
4
2
2+
Pu239primary decay is via α –decay (half life 24,000yr)

## Slide 22
Beta decay - negatron
This decay mode is characteristic of lighter, neutron-rich nuclei, high speed electron or positron
● β particles have a range of energies a few keV (3H) up to 2-3 MeV (90Y)
● Low mass, medium energy. Less damaging but ~3m in air
e.g. Tc99 , Cs134
H He + e
3
1
3
2
0
-1
-

## Slide 23
Gamma Emission
α- or β-decay can proceed via an excited state of the product nucleus. The excited state de-excites by emission of a high energy photon, a γ–ray.
The total decay energy is partitioned between the particle and the γ–ray.
For some isotopes, like 60Co, all decays give rise to γ–emission; in some (241Am, 137Cs) a proportion of decays do; in some (3H, 14C), none do.
e.g. Cs137
60Co
60Ni
100%
γ 1173 keV
β- (Emax 310 keV)
γ 1333 keV
60Co decay

## Slide 24: Stopping radiation
Sheet of paper
Aluminium sheet
Lead blocks
Modelled molecular
damage in Zircon
Damage haloes around
zircon in biotite
200μm
amorphisation

## Slide 25
Working With Radioactive Materials

## Slide 26
Where is radioactive waste from?
Nuclear
Fuel
Cycle
+
Research & Development (R&D)
RADIOACTIVE WASTE: Material that has no further use, and is contaminated by, or incorporates, activity above certain levels defined in UK legislation is known as radioactive waste.

## Slide 27: Fuel Rods: hottest properties
neutron
235U
Fission fragments
Cs, Sr, Tc, I
Short lived
Isotopes. Half-life
milleseconds
to years.
Radioactive and hot
238-241Pu
238Np
241Am
Transuranics
Long lived Isotopes. Half-life
thousands to 100s thousands of years. Radioactive and produce daughters.
2 – 3 years operations – full of breakdown products
Spent fuel = ~3% FPs; ~1% Pu; 96% 235+238U
1 million X more radioactive than they went in.

## Slide 28: Radwaste definitions
High-level waste: (HLW)
  Produces radioactivity and heat.
  From reprocessing spent fuel, nitric acid solutions and glasses
Intermediate-level waste (ILW)
  High radioactivity but little heat
  Steel, graphite, concrete, cement and sand, sludges etc. (e.g. from buildings)
Low-level waste (LLW)
  Wastes less than 4 GBqs per tonne of alpha activity or 12 Gbq per tonne of beta/gamma activity
  Plastics, paper and metal, soils, building materials and plant.
Very low-level waste (VLLW)
  Controlled or general landfill depending on volume.
https://ukinventory.nda.gov.uk/wp-content/uploads/2021/03/20201222-Official-Rep-PO023346_fact-sheet-03.pdf

## Slide 29: Volume of waste-the challenge
Approx. 450,000 m3

## Slide 30
Sellafield
70% by volume already at Sellafield
70% HLW/ILW at Sellafield (volume)
Radioactivity % much higher as all HLW and Spent Fuel is sent there

## Slide 31: So what can we do with the waste?

## Slide 32
UK 35000 TBq in the Atlantic
(USA at least ‘34282 containers’)
Sea Dumping 1948-1982
High level 1972
All wastes 1994

## Slide 33
Early bad habits!
Sellafield
Dounreay

## Slide 34
Waste at Sellafield, Cumbria

## Slide 35: Geological disposal
Multi-barrier method
  Wasteforms
  Casing for waste
  Engineered barrier system
  Geosphere
Last for 106 years

## Slide 36: Deep Geological Disposal
Should we be able to access the waste again?

## Slide 37: What do we need to know?

## Slide 38: Summary
Waste materials will take up to a million years to be considered ‘safe’
The nuclear waste comes from every part of the nuclear fuel cycle from mining the uranium to reprocessing the spent fuel
There have been many different scenarios for disposal
Deep geological disposal is the UK method
But where exactly to put it…?

## Slide 39: A Sustainable Planet
Low Carbon Energy
Dr Vicky Coker
Department of Earth and Environmental Sciences
vicky.coker@manchester.ac.uk; Williamson Building

## Slide 40: Learning outcomes
Why low carbon?
Discussion of the sources of low carbon energy
  Wind
  Hydroelectric
  Solar
  Biofuels
  Geothermal
https://www.iea.org/reports/the-role-of-critical-minerals-in-clean-energy-transitions/mineral-requirements-for-clean-energy-transitions

## Slide 41
Energy Institute Statistical Review of World Energy 2024

## Slide 42
Natural Energy Flows
Mean Solar Input 342 Wm-2 or 5500 Q/year
Earth
Atmosphere
Photosynthesis 1 Q/y
Reflected radiation (albedo 30%) 1650 Q/y
Absorption and re-radiation 3850 Q/y
Evaporation and precipitation 1300 Q/y
Solar power assoc. with winds waves and currents 12 Q/y
Geothermal outflow from Earth ~ 1 Q/y
Mean tidal power assoc with Earth-Sun-Moon ~ 0.1 Q/y
Note: 1Q = 1021J

## Slide 44: Wind turbine
Wind turbines rotor blades, made from e.g. fibreglass-reinforced polyester
30-80 m diameter
the longer the blades, the greater the energy output.
rotate at 10-30 revolutions per minute
Rotational energy is converted into electricity
Kinetic energy = 0.5mv2
m = rAv
Therefore:
KE per sec (power)
=0.5rAv3
m = mass of air through turbine
v = velocity of the air
r = density of the air
A = swept area of the turbine

## Slide 45
https://grid.iamkate.com/
https://www.renewableuk.com/energypulse/ukwed/

## Slide 46: Fluctuations
MacKay, 2009

## Slide 47: Hydroelectric power
Usually generated at large dams in order to increase the vertical drop of the water
Energy available (in J) = m x g x h
  m = mass of water available in kg
  g = acceleration due to gravity (9.81 ms-1)
  h = height differential
By using two reservoirs at different heights, water can be pumped uphill to store energy during periods of low demand

## Slide 49: Three Gorges Dam, China
Largest hydroelectric dam in the world since completion in 2012
Generating capacity of 22,500 MW
However power limited at certain times of the year due to water availability
Height =181m and over 2km in length
Creates the 3 Gorges Reservoir which extends 600 km upstream

## Slide 50: UK Hydroelectric power
Exploited in the UK
Large installations can harvest this energy very efficiently (up to 95%)
1-2% of our electricity generation
https://www.carbonbrief.org/mapped-how-the-uk-generates-its-electricity

## Slide 51: Solar power

## Slide 52: Solar electrical generation
Photovoltaic technology
Concentrated Solar Power (CSP)

## Slide 53: Photovoltaic cell
Semiconductor e.g. Silicon, GaAs, CdTe
N-type silicon: addition of impurity creates extra electrons e.g. P
P-type silicon: addition of impurity creates ‘holes’ for electrons e.g. B
Transfer of energy from the light (photon) to the extra electrons
Electrons move generating a current

## Slide 54: Biofuels and waste products
Any solid, liquid or gaseous fuel derived from recently living organisms
Using crops as a source of fuel means that any carbon released through combustion is offset by carbon absorbed as the plant grows
Can be a direct replacement for petrol/diesel or used for electricity generation

## Slide 55
Some fuels can be direct replacements for fossil fuels (e.g. biodiesel, biogas)
Some can be produced from by-products, easing the pressure on farmland used for other crops
  e.g. biogas from food waste and sewerage, wood pellets from sawdust

## Slide 56: Geothermal power

## Slide 57: Geothermal power

## Slide 58: Locations of geothermal sites
https://www.thinkgeoenergy.com/map/

## Slide 59: Distribution
The existing national grid is designed around providing the greatest generation capacity close to where demand is greatest (e.g. cities, heavy industry)
In a low-carbon scenario, many of the sources of power are far from the users of the power (e.g. tidal streams in Scotland)
Much work is needed to upgrade the power distribution network as a result

## Slide 61: Summary
Substantial amounts of energy could in theory be utilised through non-nuclear low-carbon technologies
Even with the technical capacity, many economic, social and environmental issues will likely make implementing some technologies unfeasible
Part of an energy mix

## Slide 63: World Nuclear Association
https://world-nuclear.org/
Read about your own country or one of interest
Post interesting facts related to:
  Do they use nuclear? Why/Why not?
  How are they dealing with the waste?
  Has any country completed a waste repository?
Add to mentimeter to build the discussion